## Slide 1: BORDER MONITORING WITH WIRELESS SENSOR NETWORKS
ELE 402 - Special Topics in Automation Systems
Student: Rafael Rihart Halmann
Advisor: Cel. Jorge Stoccedo
Prof.: Edison Pignaton

## Slide 2: SUMMARY
Problem definition
Simulatin environment
Metrics
Simulation setup
Simulation results

## Slide 3
Problem definition

## Slide 4: Problem Definition
Border Monitoring Characteristics:
Long distances and relative narrow range of area to be monitored;
Usually it demands high cost or even infeasible for installation of infrastructure;
Demands discretion in order to avoid being located and destroyed by the invader;
WSNs Suitability
Easy field implementation;
Centralized/Decentralized control;
Static/Mobile sink;
Auto-configurable;
Evaluate four different routing protocols (DSR, AODV, DSDV and TORA) in the application of border surveillance system in order to meet performance metrics regarding energy consumption, packet delivery ratio, end-to-end delay and throughput.

## Slide 5: motivation and Relevance
Border surveillance characteristics:
Border extensions to be monitored is about 17,000 km;
Only about 4% of our border is monitored;
Hostile and uninhabited topography;
Sparse intrusion events occurrence;
Long time interval between events;
Cost constraint;

## Slide 6
Simulatin environment

## Slide 7: SIMULATION ENVIRONMENT
NETWORK SIMULATOR (NS-2)
Environment Definition and Configuration
  Narrow and long distance area representing a border surveillance scenario [1][2];
  Simulate the intruder detection via U.S. Naval Research Laboratory extension to NS-2 (nrlsensorsim) [3]:
    PHENOM broadcast packets through a specific channel;
    Adjust the sensing sensitivity of the physical phenomenon by the transmission range of the broadcasted packets;
    Do not contributes with network overhead once PHENOM protocol works independently from the WSN protocol.

## Slide 8: SIMULATION ENVIRONMENT
NETWORK SIMULATOR (NS-2)
In order to quantitatively compare the options, four metrics have been considered based on [1], [2] and [4]:
Wireless Sensor Network Performance Metrics
  Energy Consumption (Maximum energy per node and average energy of the network)
  Packet Delivery Ration
  End-to-End Delay
  Troughput

## Slide 9: SIMULATION ENVIRONMENT
NS-2 ARCHITECTURE
Two frameworks
  C++: Low level componente definition and data processing;
  Otcl: User interface and simulation environment configuration;
Event-driven simulator;
Support for mono-thread event processing;
Support for trace file;
Graphical animation of the network;

## Slide 10: DETAILED DEFINITION OF THE PROPOSAL SOLUTION
NETWORK SIMULATOR (NS-2)
First version in 1989 based on Real Network Simulator;
Developed by Berkley University;
Open source and free for research and educational;
Discrete-event network simulator
Two languages:
  C++ for protocol implementation;
  Otcl to describe and configure the simulation environment;
IP and non-IP based networks simulation;
Support for Wi-Fi, WiMAX, or LTE for layers 1 and 2 with a variety of static or dynamic routing protocols;

## Slide 11: DETAILED DEFINITION OF THE PROPOSAL SOLUTION
NS-2 ARCHITECTURE
Phenomenon
  Use a specific channel;
  Implements its own routing protocol;
  Four diferente types of phenomenon
    CO – carbono monoxid;
    HEAVY GEO – heavy seismic activity;
    LIGHT GEO – light seismic activity;
    SOUND – audible sound;
    TEST_PHENOMENON – generic;
Steps for implementing a simulation
  Step 1: Declare simulator and output file;
  Step 2: Setting node and Link;
  Step 3: Setting agent;
  Step 4: Setting application;
  Step 5: Setting simulation time and schedulers
  Step 6: Declare finish;

## Slide 12
Metrics

## Slide 13: METRICS TO EVALUATE THE PROTOCOLS
NETWORK METRICS
End-to-End delay | Packet delivery ration (PDR)
Throughput | Energy consumption
In order to quantitatively compare the options, four metrics have been considered based on [1], [2] and [4]:

## Slide 14
Simulation setup

## Slide 15: Simulation setup
SIMULATION
Rectangle sensor area (10 km x 500 m);
Deterministic and random sensor deployment;
Protocols:
  Static and mobile sink;
  On-demand and proactive;
  DSR – Dinamic Source Routing;
  DSDV – Destination Sequence Distance Vector;
  AODV – Ad-hoc On Demand Routing Protocol;
  TORA – Temporarlly Ordered Routing Algorithm (did not work in NS-2.26 until now);
Population criterion – node density;

## Slide 16: SIMULATION SETUP
CALCULATION OF THE NODE DENSITY [1][7]
  Strong Barrier Coverage
  Weak Barrier Coverage / Orthogonal Detection

## Slide 17: SIMULATION SETUP
CALCULATION OF THE NODE DENSITY
  DetQM [7]

## Slide 18: SIMULATION SETUP
CALCULATION OF THE NODE DENSITY
  [1] M. Hammoudeh et al., “A Wireless Sensor Network Border Monitoring System: Deployment Issues and Routing Protocols”, in IEEE Sensors Journal, vol. 17, no. 8, pp. 2572-2582, 15 April15, 2017. doi: 10.1109/JSEN.2017.2672501

## Slide 19: Simulation setup
CALCULATION OF THE NODE DENSITY [1] [8]
  Radio Communication
    Probability that a node can communicate with at least one other node is derived from Poisson Distribution
  ρ is the node linear density in nodes per meter
  Rradio is the radio range in meter
  Rsensor is the sensor range in meter
  H is the field height
  According to the reference, a typical application (Rradio ≈ 2 Rsensor, Rsensor = 25 m and H = 100 m
  Pradio > PꞱ

## Slide 20: Simulation setup
SENSOR EXAMPLE
  SEGA-Node TIMS Radar
    Radar Typical Performance
      Range 35 M
      Frequency 720 MHz
      Bandwidth 80 MHz
      Tx Power 9 mW
      Voltage 3.6 V
      Current 5 mA
      Temp -40 to +80 C
      Target speed 0.1 to 40 m/s
  SEGA-Node TIMS Radar
    Radio Typical Performance
      Range 1 KM
      Frequency 315 Mhz
      Bandwidth 400 KHz
      Tx Power 2 mW
      Voltage 3.0 V
      Current 1.5 mA
      Temp -40 to +80 C
http://www.sperient.com/ (last access on 2018/12/09)

## Slide 21
Simulation results

## Slide 22: Simulation results
CONFIGURATION
Equivalent linear sensor density
Sensor range: 35 m
Radio range: 250 m
Number of sensor nodes: 40, 80, 120, 160, 200, 240 and 280
Simulation time: 500 sec

## Slide 23: Simulation results
SCENARIOS
Scenario 1
Scenario 2
Scenario 3
Deterministic sensor nodes depoloyment;
Targuet and sink nodes static;
Stochastic sensor nodes depoloyment;
Targuet and sink nodes static;
Stochastic sensor nodes depoloyment;
Targuet node static;
Sink node moving along “x” axis;

## Slide 24: Simulation results
SCENARIOS – COMPARATIVE - THROUGHPUT
SCENARIO 1
SCENARIO 2
SCENARIO 3

## Slide 25: Simulation results
SCENARIOS – COMPARATIVE – END-TO-END DELAY
SCENARIO 1
SCENARIO 2
SCENARIO 3

## Slide 26: Simulation results
SCENARIOS – COMPARATIVE – PDR
SCENARIO 1
SCENARIO 2
SCENARIO 3

## Slide 27: Simulation results
SCENARIOS – COMPARATIVE – Emax
SCENARIO 1
SCENARIO 2
SCENARIO 3

## Slide 28: Simulation results
SCENARIOS – COMPARATIVE – Eavg
SCENARIO 1
SCENARIO 2
SCENARIO 3

## Slide 29: Simulation results
SCENARIO 1
 | Throughtput [bit/sec] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 3804,22 | 3801,31 | 3170,35
80 | 3803,92 | 3774,22 | 3168,73
120 | 3803,08 | 3611,71 | 3173,31
160 | 3787,37 | 3367,91 | 3170,36
200 | 3804,41 | 3062,07 | 
240 | 3803,49 | 2729,55 | 
280 | 3803,6 | 2283,86 | 

## Slide 30: Simulation results
SCENARIO 1
 | End to End Delay [sec] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 0,010631 | 0,008497 | 0,007976
80 | 0,021532 | 0,016308 | 0,024601
120 | 0,029694 | 0,023101 | 0,046305
160 | 0,065495 | 0,027406 | 0,041421
200 | 0,051436 | 0,097641 | 
240 | 0,059681 | 0,029999 | 
280 | 0,073309 | 0,027166 | 

## Slide 31: Simulation results
SCENARIO 1
 | PDR |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 1 | 0,951789 | 1
80 | 1 | 0,809145 | 0,999503
120 | 1 | 0,706262 | 1
160 | 0,995529 | 0,615996 | 0,999503
200 | 0,999503 | 0,500994 | 
240 | 1 | 0,36332 | 
280 | 1 | 0,281312 | 

## Slide 32: Simulation results
SCENARIO 1
 | Emax [J] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 3,29796 | 3,7915 | 2,49898
80 | 4,9435 | 9,03365 | 4,81743
120 | 5,76667 | 12,4303 | 6,99889
160 | 4,93765 | 15,1591 | 5,8853
200 | 5,76968 | 17,9943 | 
240 | 5,76686 | 20,2055 | 
280 | 5,766870 | 22,5133 | 

## Slide 33: Simulation results
SCENARIO 1
 | Eavg [J] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 0,385167 | 3,61231 | 0,319702
80 | 0,420761 | 6,95888 | 0,397156
120 | 0,412583 | 10,5165 | 0,73549
160 | 0,374092 | 13,2809 | 0,467945
200 | 0,474593 | 15,9676 | 
240 | 0,440988 | 18,3344 | 
280 | 0,502662 | 20,1335 | 

## Slide 34: Simulation results
SCENARIO 2
 | Throughtput [bits/sec] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 3803,63 | 3802,46 | 3171,32
80 | 3804,58 | 3766,96 | 3170,29
120 | 3804,77 | 3597,9 | 3170,2
160 | 3804,5 | 3363,77 | 3169,73
200 | 3802,49 | 3037,54 | 
240 | 3804,19 | 2612,4 | 
280 | 3798,09 | 2028,14 | 

## Slide 35: Simulation results
SCENARIO 2
 | End to End Delay [sec] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 0,0155364 | 0,00795274 | 0,008084
80 | 0,02154 | 0,016994 | 0,019129
120 | 0,0324034 | 0,0211571 | 0,0273929
160 | 0,0351536 | 0,0262474 | 0,035773
200 | 0,054045 | 0,0290687 | 
240 | 0,056932 | 0,0290415 | 
280 | 0,069885 | 0,0244254 | 

## Slide 36: Simulation results
SCENARIO 2
 | PDR |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 1 | 0,95231 | 1
80 | 1 | 0,853877 | 1
120 | 1 | 0,747018 | 1
160 | 1 | 0,652584 | 1
200 | 0,999006 | 0,548708 | 
240 | 0,999503 | 0,389662 | 
280 | 0,998509 | 0,260934 | 

## Slide 37: Simulation results
SCENARIO 2
 | Emax [J] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 3,30231 | 3,59088 | 2,51204
80 | 5,55543 | 9,49463 | 4,99746
120 | 6,37946 | 14,4954 | 3,84762
160 | 4,73151 | 17,5074 | 5,03324
200 | 5,77038 | 20,4721 | 
240 | 5,76761 | 25,099 | 
280 | 5,76234 | 27,3819 | 

## Slide 38: Simulation results
SCENARIO 2
 | Eavg [J] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 0,233982 | 2,59037 | 0,242266
80 | 0,44958 | 7,29463 | 0,385787
120 | 0,373426 | 4,923967 | 0,25653
160 | 0,468213 | 7,89845 | 0,362658
200 | 0,427629 | 8,95975 | 
240 | 0,396824 | 10,06805 | 
280 | 0,407503 | 22,8242 | 

## Slide 39: Simulation results
SCENARIO 3
 | Throughtput [bits/sec] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 986,884 | 3522,45 | 3178,26
80 | 1048,74 | 3756,9 | 3176,07
120 | 1078,41 | 3550,74 | 3178,12
160 | 1107,68 | 2683,8 | 3178,77
200 | 1026,52 | 2229,88 | 
240 | 1042,07 | 1977,37 | 
280 | 1100,88 | 2028,14 | 

## Slide 40: Simulation results
SCENARIO 3
 | End to End Delay [sec] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 0,002072 | 0,004174 | 0,005098
80 | 0,008792 | 0,016609 | 0,010026
120 | 0,010551 | 0,021755 | 0,020293
160 | 0,009247 | 0,012009 | 0,027455
200 | 0,010374 | 0,021089 | 
240 | 0,018299 | 0,018704 | 
280 | 0,015852 | 0,024425 | 

## Slide 41: Simulation results
SCENARIO 3
 | PDR |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 0,259443 | 0,886183 | 1
80 | 0,229622 | 0,848982 | 1
120 | 0,235966 | 0,737078 | 1
160 | 0,242921 | 0,459742 | 1
200 | 0,223547 | 0,389662 | 
240 | 0,228018 | 0,319583 | 
280 | 0,241054 | 0,260934 | 

## Slide 42: Simulation results
SCENARIO 3
 | Emax [J] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 2,50647 | 2,53146 | 1,52791
80 | 5,7795 | 9,44977 | 2,78052
120 | 4,36316 | 14,1429 | 3,09319
160 | 5,55477 | 18,9066 | 4,85449
200 | 5,99979 | 25,738 | 
240 | 5,765 | 27,7664 | 
280 | 5,76608 | 27,3819 | 

## Slide 43: Simulation results
SCENARIO 3
 | Eavg [J] |  | 
Nº Nodes | AODV | DSDV | DSR
40 | 0,247702 | 2,47462 | 0,164301
80 | 0,401848 | 7,27264 | 0,217044
120 | 0,302166 | 11,1413 | 0,211215
160 | 0,393544 | 14,3279 | 0,322888
200 | 0,405801 | 19,3771 | 
240 | 0,411209 | 21,9111 | 
280 | 0,397026 | 22,8242 | 

## Slide 44: Simulation results
NEXT STEPS
Add more protocols in the evaluation scope;
Different node deployment strategies;
Improve energy model;

## Slide 45: references
[1] M. Hammoudeh et al., “A Wireless Sensor Network Border Monitoring System: Deployment Issues and Routing Protocols”, in IEEE Sensors Journal, vol. 17, no. 8, pp. 2572-2582, 15 April15, 2017. doi: 10.1109/JSEN.2017.2672501
[2] Sharei, Hoda & Keshavarz-Haddad, Alireza & Garraux, Gaëtan, “Routing Protocols for Border Surveillance Using ZigBee-Based Wireless Sensor Networks”, Communications in Computer and Information Science. 370, 2013, pp. 114-123. 10.1007/978-3-642-38865-1_13.
[3] Downard, Ian, “Simulating sensor networks in ns-2”, Network and Communication Systems Information Technology Division – U.S. Naval Research Laboratory, may 31 2004, NRL/FR/5522--04-10,073
[4] Anil Saini, Anil Kumar, “Performance Analysis of Routing Protocols in Mobile Ad-hoc Networks Using NS2”, ICETEST Track , International Journal on Future Revolution in Computer Science & Communication Engineering march 2018 volume 4 issue 3 (IJFRSCE), PP: 150 – 154
[5] Khan, Majid I., Wilfried N. Gansterer, and Guenter Haring. “Static vs. Mobile Sink: The Influence of Basic Parameters on Energy Efficiency in Wireless Sensor Networks.” Computer Communications 36.9 (2013): 965–978. PMC. Web. 21 Sept. 2018.
[6] Keerthika, A., Berlin Hency, V., “A survey of routing protocols of wireless sensor network with mobile sinks.” ARPN J. Eng. Appl. Sci. 11(11), 6951–6963, 2016.
[7] Komar, C., 2012, “Detection Quality Measure in Surveillance Wireless Sensor Networks”, PhD Thesis, Boğaziçi University, Istanbul, Turkey.
[8] Senouci, Mustapha & Mellouk, Abdelhamid & Aissani, Amar. “Random deployment of wireless sensor networks: A survey and approach”. Int. J. of Ad Hoc and Ubiquitous Computing. 15. 133 – 146, (2014). 10.1504/IJAHUC.2014.059905.